## Slide 2: طراحي کامپيوتري سيستم هاي ديجيتال
حل چند مثال
پاييز 96

## Slide 3: مثال1: طراحي ديکدر باينري 2 به 4 همراه با خط فعال ساز

## Slide 4: حل مثال 1: توصيف data flow
Library ieee;
Use ieee.std_logic_1164.all;
Entity DEC24 is
port( I : in std_logic_vector(1 downto 0);
EN: in std_logic;
Y: out std_logic_vector(3 downto 0));
End;
Architecture dec2to4 of DEC24 is
Begin
Y(0) <= (NOT I(0)) and (NOT I(1)) and EN;
Y(1) <= I(0) and (NOT I(1)) and EN;
Y(2) <= (NOT I(0)) and I(1) and EN;
Y(3) <= I(0) and I(1) and EN;
End;

## Slide 5: حل مثال 1: با استفاده از دستور when … else
Library ieee;
Use ieee.std_logic_1164.all;
Entity DEC24 is
port( I : in std_logic_vector(1 downto 0);
EN: in std_logic;
Y: out std_logic_vector(3 downto 0));
End;
Architecture dec2to4 of DEC24 is
Begin
Y <= "0001" when I="00" and (EN='1') else
"0010" when I="01" and (EN='1') else
"0100" when I="10" and (EN='1') else
"1000" when I="11" and (EN='1') else
"0000" ;
End;

## Slide 6: حل مثال 1: با استفاده از دستور process
Library ieee;
Use ieee.std_logic_1164.all;
Entity DEC24 is
port( I : in std_logic_vector(1 downto 0);
EN: in std_logic;
Y: out std_logic_vector(3 downto 0));
End;
Architecture dec2to4 of DEC24 is
Begin
process (I,EN)
begin
if EN=‘0’ then Y <= "0000“;
elsif I="00" then Y <= “0001”;
elsif I="01" then Y <= “0010”;
elsif I="10" then Y <= “0100”;
else Y<= “1000”;
end if;
end process;
End;

## Slide 7: مثال 2- طراحي رمزگشاي 3 به 8 با استفاده از دو رمز گشاي 2 به 4
Library ieee;
Use ieee.std_logic_1164.all;
Entity DEC38 is
port( S: in std_logic_vector(2 downto 0);
Q: out std_logic_vector(7 downto 0));
End;
Architecture dec3to8 of DEC38 is
component DEC24 port(I : in std_logic_vector(1 downto 0);
EN: in std_logic;
Y: out std_logic_vector(3 downto 0));
End component;
signal ns: std_logic;
Begin
ns<= not s(2);
DEC1: DEC24 port map(I(1)=>S(1), I(0)=>S(0), En=> ns, Y(3)=>Q(3),Y(2) =>Q(2), Y(1)=>Q(1), Y(0)=> Q(0));
DEC2: DEC24 port map(I(1)=>S(1), I(0)=>S(0), En=> S(2), Y(3)=>Q(7),Y(2) =>Q(6), Y(1)=>Q(5), Y(0)=> Q(4));
End;

## Slide 8: نتيجه شبيه سازي مثال2

## Slide 9: مثال3: طراحي full adder با استفاده از dec3to8

## Slide 10: حل: توصيف ساختاري
Library ieee;
Use ieee.std_logic_1164.all;
Entity FA is
port( x,y,z: in std_logic;
Sum,cout: out std_logic);
End;
Architecture fulladder of FA is
component DEC38 port( S: in std_logic_vector(2 downto 0);
Q: out std_logic_vector(7 downto 0));
End component;
signal m: std_logic_vector(7 downto 0);
Begin
DEC: DEC38 port map(s(2)=>x, s(1)=>y, s(0)=>z, Q(7)=>m(7), Q(6)=>m(6), Q(5)=>m(5),
Q(4)=> m(4), Q(3)=>m(3), Q(2)=>m(2), Q(1)=>m(1), Q(0)=>m(0));
sum <= m(1) OR m(2) OR m(4) OR m(7);
cout <= m(3) OR m(5) OR m(6) OR m(7);
End;

## Slide 11: طراحي دي مالتي پلكسر1 به 4 با خط فعال ساز با استفاده از ديکدر 2 به 4
S0 s1
Y0
Y1
Y2
Y3
D
E
m0
m1
m2
m3
2-to-4 Decoder
فعال ساز

## Slide 12: مثال5: طراحي ديکدر 4 به 16 با استفاده از اتصال درختي 5 ديکدر 2 به 4 با خط فعال ساز.
Library ieee;
Use ieee.std_logic_1164.all;
Entity DEC416is
port( a,b,c,d,en1: in std_logic;
Q: out std_logic_vector(15 downto 0));
End;
Architecture dec4to16 of DEC416 is
component DEC24 port(I : in std_logic_vector(1 downto 0);
EN: in std_logic;
Y: out std_logic_vector(3 downto 0));
End component;
signal e: std_logic_vector(3 downto 0);
Begin
DEC1: DEC24 port map(I(1)=>a, I(0)=>b, En=>en1, Y(3)=>e(3),Y(2) =>e(2), Y(1)=>e(1), Y(0)=> e(0));
DEC2: DEC24 port map(I(1)=>c, I(0)=>d, En=> e(0), Y(3)=>Q(3),Y(2) =>Q(2), Y(1)=>Q(1), Y(0)=> Q(0));
DEC3: DEC24 port map(I(1)=>c, I(0)=>d, En=> e(1), Y(3)=>Q(7),Y(2) =>Q(6), Y(1)=>Q(5), Y(0)=> Q(4));
DEC4: DEC24 port map(I(1)=>c, I(0)=>d, En=> e(2), Y(3)=>Q(11),Y(2) =>Q(10), Y(1)=>Q(9), Y(0)=> Q(8));
DEC5: DEC24 port map(I(1)=>c, I(0)=>d, En=> e(3), Y(3)=>Q(15),Y(2) =>Q(14), Y(1)=>Q(13), Y(0)=> Q(12));
End;

## Slide 13
-Seven Segment Decoder

## Slide 14
Library ieee;
Use ieee.std_logic_1164.all;
Entity seven_seg is
port( a: in std_logic_vector(3 downto 0);
z: out std_logic_vector(6 downto 0);
End;
Architecture with_select of seven_seg is
Begin
with a select
z <= “1111110” when “0000” ,
“0110000” when “0001” ,
“1101101” when “0010” ,
“1111001” when “0011” ,
“0110011” when “0100” ,
“1011011” when “0101” ,
“1011111” when “0110” ,
“1110000” when “0111” ,
“1111111” when “1000” ,
“1111011” when “1001” ,
“0000000” when others ;
End;

## Slide 15: - طراحی انکدر اولويت دار 4 به 2
وروديها |  |  |  | خروجي‌ها |  | 
D0 | D1 | D2 | D3 | Y1 | Y0 | V
0 | 0 | 0 | 0 | X | X | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
X | 1 | 0 | 0 | 0 | 1 | 1
X | X | 1 | 0 | 1 | 0 | 1
X | X | X | 1 | 1 | 1 | 1

## Slide 16
Library ieee;
Use ieee.std_logic_1164.all;
Entity priority is
port( D: in std_logic_vector(3 downto 0);
y: out std_logic_vector(1 downto 0),
v: out std_logic);
End;
Architecture EN of priority is
Begin
y <= “11” when D(3) = ‘1’ else
“10” when D(2) = ‘1’ else
“01” when D(1) = ‘1’ else
“00” when D(0) = ‘1’ else
“00”;
v <= D(0) or D(1) or D(2) or D(3);
End;